## Slide 1
NRCS AWDB
ColoradoWaterSMS
01-Download Natural Flow Time Series
02-Download Reservoir Storage Time Series
04-Download Forecast Time Series
ColoradoWaterHBGuest
START
Data Download Processes
Output files are located in Input-TimeSeries-Raw directory and are organized by data type folders (ForecastedNaturalFlow, NaturalFlow, and ReservoirStorage).
Outputs from Step 01 in the Input-TimeSeries-Raw\NaturalFlow directory include:
  Intermediate files for daily and monthly observed flow data from DWR (ObservedFlow-DWR-Day.DV and ObservedFlow-DWR-Month.DV).
  Excel file with all monthly natural and observed flow data (Flow-Month.xlsx).
Outputs from Step 02 in the Input-TimeSeries-Raw\ReservoirStorage directory include:
  An intermediate file for daily reservoir data from DWR data sources (ReservoirStorage-DWR-Day.DV).
Outputs from Step 04 in the Input-TimeSeries-Raw\ForecastedNaturalFlow directory include:
  An intermediate file with all NRCS 50% forecasts for all queried forecast periods (NRCS50PercentForecasts.xlsx).
Go To Data Check and Filling Processes
NaturalFlow/NaturalFlow-Month
TS Alias = {stationId}-NaturalFlow-Month
TS Properties = stationId, stationName, dataSource, SWSIBasin2
Data Flags = none
ReservoirStorage/ReservoirStorage-Month
TS Alias = {stationId}-ReservoirStorage-Month
TS Properties = stationId, stationName, dataSource
Data Flags = E (assigned by NRCS)
ForecastedNaturalFlow/ForecastedNaturalFlow-Month
TS Alias = {stationId}-ForecastedNaturalFlow-Month
TS Properties = stationId, stationName
Data Flags = none
NaturalFlow/ObservedFlow-Month
TS Alias = {stationId}-ObservedFlow-Month
TS Properties = stationId, stationName, dataSource
Data Flags = HB (ColoradoWaterHBGuest), SMS (ColoradoWaterSMS)

## Slide 2
20-Check Raw Time Series
25-Fill Data Auto
Data Download Processes
Data Check and Filling Processes
Output data files are located in Input-TimeSeries-Raw directory and are organized by data type folders (ForecastedNaturalFlow, NaturalFlow, and ReservoirStorage).
Outputs from Step 25 in the Input-TimeSeries-Raw\NaturalFlow directory include:
  Intermediate files for the data used for filling (NaturalFlow-Month-1AutoFillingData.DV and ObservedFlow-Month-1AutoFillingData.DV.
An Excel workbook is written with the final input data that includes all data flags (Input-Data-Final.xlsx).
Go To Create SWSI Component Processes
NaturalFlow/NaturalFlow-Month-1AutoFill
TS Alias = {stationId}-NaturalFlow-Month
TS Properties = stationId, stationName, dataSource, SWSIBasin2
Data Flags = R (Regression), RZ (Regression value replaced with zero)
ReservoirStorage/ReservoirStorage-Month-1AutoFill
TS Alias = {stationId}-ReservoirStorage-Month
TS Properties = stationId, stationName, dataSource
Data Flags = E (assigned by NRCS), Z (Zero), I (Interpolate), H (Historical Averages)
RawTimeSeriesChecks.xlsx
ReservoirStorage/ReservoirStorage-Month
TS Alias = {stationId}-ReservoirStorage-Month
TS Properties = stationId, stationName, dataSource
Data Flags = E (assigned by NRCS)
ForecastedNaturalFlow/ForecastedNaturalFlow-Month
TS Alias = {stationId}-ForecastedNaturalFlow-Month
TS Properties = stationId, stationName
Data Flags = none
27-Fill Data Manual
NaturalFlow/NaturalFlow-Month-2ManualFill
TS Alias = {stationId}-NaturalFlow-Month
TS Properties = stationId, stationName, dataSource, SWSIBasin2
Data Flags = R (Regression), RZ (Regression value replaced with zero), MO-* (Override Comments)
ReservoirStorage/ReservoirStorage-Month-2ManualFill
TS Alias = {stationId}-ReservoirStorage-Month
TS Properties = stationId, stationName, dataSource
Data Flags = E (assigned by NRCS), Z (Zero), I (Interpolate), H (Historical Averages), MO-* (Override Comments)
ForecastedNaturalFlow/ForecastedNaturalFlow-Month-2ManualFill
TS Alias = {stationId}-ForecastedNaturalFlow-Month
TS Properties = stationId, stationName
Data Flags = MO-* (Override Comments)
NaturalFlow/NaturalFlow-Month
TS Alias = {stationId}-NaturalFlow-Month
TS Properties = stationId, stationName, dataSource, SWSIBasin2
Data Flags = none
NaturalFlow/ObservedFlow-Month
TS Alias = {stationId}-ObservedFlow-Month
TS Properties = stationId, stationName, dataSource
Data Flags = HB (ColoradoWaterHBGuest), SMS (ColoradoWaterSMS)
NaturalFlow/ObservedFlow-Month-1AutoFill
TS Alias = {stationId}-ObservedFlow-Month
TS Properties = stationId, stationName, dataSource
Data Flags = HB (ColoradoWaterHBGuest), SMS (ColoradoWaterSMS), R (Regression), RZ (Regression value replaced with zero)
NaturalFlow/ObservedFlow-Month-2ManualFill
TS Alias = {stationId}-ObservedFlow-Month
TS Properties = stationId, stationName, dataSource
Data Flags = HB (ColoradoWaterHBGuest), SMS (ColoradoWaterSMS), R (Regression), RZ (Regression value replaced with zero), MO-* (Override Comments)

## Slide 3
30-CreateTimeSeriesForSWSI
Data Check and Filling Processes
Create SWSI Component Processes
Output files are located in Input-TimeSeries-ForSWSI directory and are organized by component type folders (ForecastedRunoff, PrevMoStreamflow, and ReservoirStorage).
A summary of the component data is written to SWSI-Components-Data.xlsx.
Go To SWSI Calculation Processes
ReservoirStorage/SWSI-Component-ReservoirStorage
TS Alias = {stationId}-Component-ReservoirStorage
TS Properties = stationId, stationName
Data Flags = E (assigned by NRCS), Z (Zero), I (Interpolate), H (Historical Averages), MO-* (Override Comments), M (Missing)
ReservoirStorage/ReservoirStorage-Month-2ManualFill
TS Alias = {stationId}-ReservoirStorage-Month
TS Properties = stationId, stationName, dataSource
Data Flags = E (assigned by NRCS), Z (Zero), I (Interpolate), H (Historical Averages), MO-* (Override Comments)
ForecastedNaturalFlow/ForecastedNaturalFlow-Month-2ManualFill
TS Alias = {stationId}-ForecastedNaturalFlow-Month
TS Properties = stationId, stationName
Data Flags = MO-* (Override Comments)
NaturalFlow/SWSI-Component-ForecastedRunoff
TS Alias = {stationId}-Component-ForecastedRunoff
TS Properties = stationId, stationName
Data Flags = MO-* (Override Comments), M (Missing)
Note: where historical natural flow data are used, data flags have been lost due to accumulations over the forecast period
PrevMoStreamflow/SWSI-Component-PrevMoStreamflow
TS Alias = {stationId}-Component-PrevMoStreamflow
TS Properties = stationId, stationName, FlowType
Data Flags = HB (ColoradoWaterHBGuest), SMS (ColoradoWaterSMS), R (Regression), RZ (Regression value replaced with zero), MO-* (Override Comments), M (Missing)
NaturalFlow/Station-ForecastedRunoff-PctOfAverage
TS Alias = {stationId}-ForecastedRunoff-PctOfAverage
TS Properties = stationId, stationName
Data Flags = none
ReservoirStorage/Station-ReservoirStorage-PctOfAverage
TS Alias = {stationId}-ReservoirStorage-PctOfAverage
TS Properties = stationId, stationName
Data Flags = none
PrevMoStreamflow/Station-PrevMoStreamflow-PctOfAverage
TS Alias = {stationId}-PrevMoStreamflow-PctOfAverage
TS Properties = stationId, stationName, FlowType
Data Flags = none
NaturalFlow/NaturalFlow-Month-2ManualFill
TS Alias = {stationId}-NaturalFlow-Month
TS Properties = stationId, stationName, dataSource, SWSIBasin2
Data Flags = R (Regression), RZ (Regression value replaced with zero), MO-* (Override Comments)
NaturalFlow/ObservedFlow-Month-2ManualFill
TS Alias = {stationId}-ObservedFlow-Month
TS Properties = stationId, stationName, dataSource
Data Flags = HB (ColoradoWaterHBGuest), SMS (ColoradoWaterSMS), R (Regression), RZ (Regression value replaced with zero), MO-* (Override Comments)

## Slide 4
50-CalculateSWSI-HUC
Create SWSI Component Processes
SWSI Calculation Processes
All graphical and tabular outputs are located in the Results-Web folder.
The SWSI-Current-Summary.xlsx file is the main output that is loaded into HydroBase by DWR.
Go To Optional Processes
55-CalculateSWSI-Basin
SWSI-Current-Summary.xlsx
HUC-{HUCID}-SWSI-history-graph.png
{HUCID}-SWSI.xlsx
{BasinName}-SWSI.xlsx
Basin-{BasinName}-SWSI-history-graph.png
ReservoirStorage/SWSI-Component-ReservoirStorage
TS Alias = {stationId}-Component-ReservoirStorage
TS Properties = stationId, stationName
Data Flags = E (assigned by NRCS), Z (Zero), I (Interpolate), H (Historical Averages), MO-* (Override Comments), M (Missing)
NaturalFlow/SWSI-Component-ForecastedRunoff
TS Alias = {stationId}-Component-ForecastedRunoff
TS Properties = stationId, stationName
Data Flags = MO-* (Override Comments), M (Missing)
Note: where historical natural flow data are used, data flags have been lost due to accumulations over the forecast period
PrevMoStreamflow/SWSI-Component-PrevMoStreamflow
TS Alias = {stationId}-Component-PrevMoStreamflow
TS Properties = stationId, stationName, FlowType
Data Flags = HB (ColoradoWaterHBGuest), SMS (ColoradoWaterSMS), R (Regression), RZ (Regression value replaced with zero), MO-* (Override Comments), M (Missing)
NaturalFlow/Station-ForecastedRunoff-PctOfAverage
TS Alias = {stationId}-ForecastedRunoff-PctOfAverage
TS Properties = stationId, stationName
Data Flags = none
ReservoirStorage/Station-ReservoirStorage-PctOfAverage
TS Alias = {stationId}-ReservoirStorage-PctOfAverage
TS Properties = stationId, stationName
Data Flags = none
PrevMoStreamflow/Station-PrevMoStreamflow-PctOfAverage
TS Alias = {stationId}-PrevMoStreamflow-PctOfAverage
TS Properties = stationId, stationName, FlowType
Data Flags = none
{BasinName}-TimeSeries.xlsx
{HUCID}-TimeSeries.xlsx
HUC-{HUCID}-SWSI-recent-graph.png
HUC-{HUCID}-SWSI-history-{month}-graph.png

## Slide 5
Optional Processes
Optional Processes
END